SAFE SYSTEM OF WORK

(Incorporating Method Statement, Risk Assessments & COSHH)

| Project Title | Site Location | Client Ref: |
| --- | --- | --- |
| SW Pan Rocks Outfalls | At rear of car park off North Shore Road Troon | SW001 |
| Scope of Work: | Detail: | This method statement relates to, carrying out upgrading works to 2No outfall pipes |
|  | Start Date: | TBC | Duration: | 3-4 weeks |
|  | Required Permits: | Permit to dig (Ground Disturbance Permit) |
|  | Statutory Notifications: | Marine Licence? ATC Council Permissions |

|  | Name | Position | Signature | Date |
| --- | --- | --- | --- | --- |
| Prepared By: | Jim McCarvill | Site Manager |  | 10/09/20 |
| Site Agent Approval |  |  |  |  |  |
| Revisions: |  |  |  |  |  |
| Comments: |  |  |

NOTE: The above revision table can be used for commenting on risk assessments/method statements from sub-contractors.

INDEX

| 1 | Health & Safety Risk Assessments |
| --- | --- |
| 2 | Environmental Risk Assessments |
| 3 | COSHH Assessments |
| 4 | Personal Protective Equipment |
| 5 | Public Interface/Third Party/Client |
| 6 | Emergency Arrangements |
| 7 | Monitoring & Compliance |
| 8 | Resources Required |
| 9 | Methodology (Method Statement) |
| 10 | Communication |

| SECTION 1: | HEALTH & SAFETY RISK ASSESSMENTS |
| --- | --- |
| Cross reference to relevant site-specific risk assessments |
| Abrasive wheels | Portable tools (PUWER | Services (buried & overhead) |
| Slips, trips & falls | Loading/offloading materials | Lifting operations |
| Excavations and pipe-laying | Manual handling | Work in inclement weather |
| Noise & vibration on site | Traffic/pedestrian management | COVID 19 |
| Tidal work |  |  |

| SECTION 2: | ENVIRONMMENTAL RISK ASSESSMENTS |
| --- | --- |
| Cross reference to relevant site-specific risk assessments |
| Nuisance (dust, emissions etc) | Nuisance (noise and vibration) | Refuelling |
| Waste Management (storage) | Waste Management (disposal) | Water – Pollution |
| Spill response | Public relations |  |

| SECTION 3: | COSHH ASSESSMENTS |
| --- | --- |
| Cross reference to relevant site specific COSHH assessments |
| Survey paint |  |  |
| Engine oil |  |  |
| Gear oil |  |  |
| Natural aggregates |  |  |
| Stihl saw oil |  |  |
| Ready Mixed Concrete |  |  |

| SECTION 4: | PERSONAL PROTECTIVE EQUIPMENT |
| --- | --- |
| Hard hat, hi-visibility clothing, steel toe capped safety footwear & gloves as standard. Detail other PPE required from the risk assessments. |
| Hearing protection (proximity to noisy plant) | Mask (FFP3) using Stihl Saw Facemasks/gloves (Covid) |
| Site operatives to remain vigilant to detect unpleasant odours, coloured fill, fibrous material, or chemical residues | Eye protection (mandatory on all GL sites) |

| SECTION 5: | PUBLIC INTERFACE/THIRD PARTY/CLIENT |
| --- | --- |
| Highlight significant management issues | Detail how these issues are to be managed |
| Public interface and protection. | All construction vehicles will be turned and guided by banksmen and reversed into the site. All necessary steps will be taken to protect the public from the works. All construction work will be undertaken within the site boundaries which will be fenced off using 2m high clipped Heras fence panels. The Heras fence will be double clipped as added security. |
| Site access / egress | Access shall be from the car park |
| Services | GL shall remain aware of the possibility of unknown public and private services within the site boundary and shall remain entirely responsible for locating and identifying throughout the duration of the works. All existing services are always to be maintained during the works. |

| SECTION 6: | EMERGENCY ARRANGEMENTS (first aid, rescue procedures, environmental etc.) |
| --- | --- |
| In the event of an emergency on-site, all operatives should convene at the muster point in the work area Identify fire routes and display notices. Position fire extinguishers at strategic points. Inform all employees of the above. Site manager is to be informed immediately of all emergencies or incidents. Emergency contacts notice, details of First Aiders & Fire Action signs on display in folder. Fire Station – Fire & Rescue Service, 106 Portland Street, Troon KA10 6QN – 999 or 01292 310715 Police Station – Police Scotland 116 Portland Street, Troon KA10 6QU– 999 or 01292 310100 Nearest A&E Hospital: Crosshouse Hospital Kilmarnock KA02 0BE – 999 or 01563 B.T – 0800 917 3993 Scottish Water – 0845 603 8855 Scottish Power – 0845 272 7999 SGN – 0800 111 999 (gas escapes) SEPA will be contacted by the Client (East Dunbartonshire Council) with a view to agreement on managing the environmental risk for these activities on site. G.L. site manager will liaise with SEPA to ensure that the environmental risk of the activities is minimised. SEPA – 0800 807 060 Pollution of any watercourse and/or marine environment with construction debris is to be avoided always. Noise and dust to be kept to a minimum. Damping down of the work area with water will be undertaken if required to prevent excess dust. The ganger is a fully qualified First Aider and the site manager has attended the one-day course and is an “Appointed Person”. First aid boxes will be readily available in site transport. Refuelling of machines will be undertaken above a drip tray. Spill kits available however for major spills contact should be made with specialists: KN Services 01821 640201. All surplus material from excavation work will be transported to a licensed waste disposal site. No material will be removed off site without the written permission from the engineer. |

| SECTION 7: | MONITORING & COMPLIANCE |
| --- | --- |
| Detail site management & supervision who will carry out inspections to ensure compliance with this Safe System of Work |
| Daily: | Site Foreman | Weekly: | Site Agent (Jim McCarvill) |
| Others/comments The location of accommodation, unloading and storage areas shall be identified and agreed with the client (if required). Site accommodation/welfare facilities shall comply with current health and safety legislation and will be located to avoid nuisance to neighbouring land users. Secure office and non-smoking/smoking facilities etc. will be provided by GL (if required). Daily excavation inspection by ganger / site manager recorded in register. All plant and machinery to be operated by trained and authorised personnel. Labour and plant certificates to be retained in the site file. Machine Operator to complete weekly inspections of excavator and associated lifting equipment. All operatives encouraged to observe risks constantly by raising to supervision/management (“Don’t Look Away” cards). All personnel involved in these operations will be fully briefed on this safe system of work by GL site engineer and will sign the briefing form. Prior to any work commencing a review of utilities drawings will be undertaken to establish the presence of services which may affect the works, as well as a check using a CAT scan to verify the position of live services. GL site manager will give a toolbox talk to advise all operatives of the scope of works and the way they must conduct themselves on site to ensure all safe working procedures are adopted, and that their responsibilities to their fellow workmen are clearly understood. Liaison prior to work commencing shall be between GL (Jim McCarvill) and SW representative (Mark Green). Prior to works being carried out a protected species and nesting bird survey is to be carried out Additional liaison will be required between GL, Ayrshire Council and the local landowners prior to work commencing in these areas. |

| SECTION 8: | RESOURCES REQUIRED |
| --- | --- |
| Personnel: | All work will be undertaken by GL operatives. Pedestrian management measures and banksmen duties will be implemented by GL All GL operatives will be trained to operate plant as required |
| Time: | The works will take place during normal site hours. 08.00 to 16.30 Monday to Thursday 08.00 to 15.30 Friday Weekends as and when required (on instruction from SW) The programme will be based on this section of the works commencing on TBC for a duration of 4 weeks . |
| Supervision: | All activities will be overseen by GL site manager/foreman. |
| Plant/Equipment: | The following plant is to be used for these operations: Hiab excavator 7.5t lorry, Compressor c/w heavy and light breaker, Jetvac Unit/CCTV Pumps Stihl saw, Welfare van Cable avoidance tool and signal generator, Various handheld small plant, shovels, picks etc, Additional plant may be required as work progresses, |
| Materials: | Pipe/concrete/fittings/shuttering plus misc items |

| SECTION 9: | METHODOLOGY |
| --- | --- |
| Method Statement/Sequence of Task: This Method Statement relates to repair works to existing SW outfalls on the beach |
| Traffic Management |
| Work area will be set up and will be set-up and signage placed |
| Location of Works |
| The 2No outfall pipes are situated approx. 10-15m from the edge of the car park |
| This area will be fenced off using heras anti climb fence panels |
| All vehicle movements will be controlled by a banksman as the beach area is popular with dog walkers. |
| The footpaths and land are owned and maintained by North Ayrshire Council. |
| Notice is to be served on the council by Scottish Water and the area is to be signposted prior to the works taking place advising the public to take head of warning signs and instructions by the banksman. |
| Take pre-start photos of works area. |
| Refer to utility drawings supplied by the client, inspect beach area + carry-out CAT scan - record/mark all services |
| Identification of buried services will be undertaken by obtaining service drawings, surveys by authorised trained persons using CAT & Genny and all identified services will be clearly marked on the ground. |
| Safe digging techniques to be used in compliance with the Ground Disturbance Permit the contents of which must always be followed. Existing services in dig will be protected and supported. |
| Outfall 1 – High Level |
| This end of this pipe is currently buried just beneath the sand |
| The end of the pipe will be located by using a metal detector then, then excavator to expose |
| Once exposed the end of the pipe will be trimmed off to allow connection of a new section of pipe |
| The pipe will be extended by approximately 4-5m to bring it in line with and existing council outfall pipe |
| Once it has been extended a shutter will be erected to form a concrete surround to the pipe to allow for fitting of a flap valve – joints in shutter to be sealed with mastic |
| The shutter will be filled by using the excavator bucket from the edge of the car park to the work area |
| Once the concrete has cured and reached its required strength the new flap valve will be fitted |
| Area round pipe will be reinstated |
| Outfall 2 – Low Level |
| This work involves the removal of the existing flap valve and the fitting of a new flap valve |
| To carry out this work a sandbag cofferdam will be formed using ton bags lifted into position by excavator and gaps filled in with smaller bags around the mouth of the pipe outlet |
| This will allow operatives to remove the old valve by cutting off using grinders (generator pack sited in car park) |
| The new flab valve will then be fitted by drilling and fixing to the existing concrete |
| The sandbag cofferdam will then be removed |
| Site cleared |

| Section 10: Communication |
| --- |
| Highlight below the key points to be included in the safe system of work briefing to operatives. These should be extracted from relevant sections of this safe system of work and associated site-specific risk/COSHH assessments. |
| RISKS IDENTIFIED | RISK CONTROLS TO BE BRIEFED TO OPERATIVES |
| Abrasive Wheels | Only trained persons to use wheels who have been authorised by site management Keep the area clear of personnel not actively engaged in the operation Inspect prior to use that the wheel selected for the job is non-defective/correct type & guard in position Ensure there is no loose clothing or jewellery etc that could get caught up in the machine Wear a mask (FFP3), face/eye protection (EN166-B) & ear defenders in addition to standard PPE |
| Excavations | Prevent surface water run-off into the excavation Edge protected with rigid barriers must secure & maintained Work is on the beach |
| Pedestrian Management | Fencing and signage to be erected |
| Manual Handling | Ascertain information on the load to be lifted such as weight, (maximum weight 20kg men and 12 kg women) shape irregularities (bulky/unwieldy), difficult to grasp, unstable with contents likely to shift, sharp, hot or potentially damaging. Keep access routes free from obstruction and clearing up spillages Wearing appropriate Personal Protective Equipment including gloves, hard hat, hi-visibility clothing and safety footwear as a minimum Manual handling instruction and training to operatives on the priority for mechanical lifting and safe lifting techniques |
| Noise & Vibration | Adhere to noise conditions/controls as conveyed at site induction Wear good warm gloves when holding vibrating equipment Follow the traffic lights system (5B-10) High RED Consult H&S manager/adviser for advice Medium AMBER Control exposure to 2 hours maximum Low GREEN Control exposure to 8 hours maximum |
| Plant | Plant must not approach too close to an excavation such that there is a risk of collapse from a surcharge Operators must comply with instructions given & the Ground Disturbance Permit |
| Portable Tools | All operators to be trained and competent in the use of portable tools with valid certificates where appropriate PPE must be worn i.e. hard hat, safety boots, Hi Vis clothing, gloves, ear protection, respirators etc. |
| Buried Services | Ground Disturbance Permit (5D-09) to be signed prior to commencing work Always use a CAT & Genny before digging – do not make assumptions – services can rise to shallow depths |
| Spill Response | Spill kits must be used if a spillage occurs |
| Nuisance (Dust) | Ensure cutting and grinding operations are adequately shielded or wetted Keep to site speed limits to minimise dust generation Engines to be switched off when not in use |
| Refuelling | Plant shall be re-fuelled at the designated area over an impermeable surface. Return spare fuels and oils to proper storage areas Use funnels when refuelling small plant and equipment to avoid spillages Ask your site manager what to do with waste oil, petrol and diesel prior to any disposal |
| Waste Disposal | Waste Transfer Note will be required and must accompany any waste. |
| COVID 19 | All as per attached documents F1-01a, RA023 Risk assessment and additional induction for COVID (5G-04a) |
| COVID: PREVENTING THE SPREAD |
| Activity | Hygiene | Social Distancing |
| Approaching site | Sanitising station in welfare van | Manned security preventing public from entering lane |
| Site set up/remove | Gloves/wipes for barriers | No close working required – keep 2m apart. |
| Vehicles- getting to site. | Keep vehicles clean – COVID induction. | 1 driver 1 vehicle policy except welfare van having 2, who are more 2m apart. |
| General | Washing facilities in welfare van & hand gel issued. | COVID induction instructing 2m apart. Achievable in practical work. |
| Authorised visitors | COVID induction sent in advance of visit | Contact GL Supervisor on arrival in car. |
| Welfare van | Hygiene station | Only one person at each section at any one time i.e. drivers area, rest area and toilet. |
| Smoking | No smoking policy | No smoking policy |
| Emergencies | Additional PPE for first aiders as per risk assessment. | As per induction & additional PPE |
| Excavation | Hygiene station | No close working required – keep 2m apart. |
| Person giving the briefing to record who attended (no signature required from attendees) DATE ATTENDEES INSTRUCTOR |